## Slide 1
Design and Simulation of an
Automatic Street Light Control System
01
DDCA PROJECT
Digital logic model in Logisim
Students: [Names and roll numbers]
Guide: [Guide name]
Department: [Department] College: [College]
Academic year: [Academic year] Team: [Team ID]
Notes: New reference implementation prepared for the project topic. Replace all bracketed identity fields before submission. This deck describes a digital model, not a completed physical street-light installation.

## Slide 2
Introduction
02
Application
Street lights should respond to changes in ambient light.
Digital model
A binary daylight input represents the output of a light-sensing stage.
Control rule
In automatic mode, darkness turns the lamp ON and daylight turns it OFF.
DDCA concepts
Boolean algebra, combinational gates and truth-table verification.
Notes: Assumed sensor convention: D=1 means daylight and D=0 means darkness. Logisim input pins stand in for sensor electronics.

## Slide 3
Problem statement
03
How can a simple logic circuit switch a street light according to daylight?
Manual operation
A person must switch the lamp at the appropriate time.
Required behavior
Provide automatic switching, a master disable and a manual ON command.
Project boundary
Model logical decisions. Sensor voltages, lamp power and energy savings require separate hardware tests.

## Slide 4
Objectives
04
01 Define inputs
Specify daylight D, master enable E and manual ON M.
02 Derive logic
Implement L = E AND ((NOT D) OR M).
03 Build the circuit
Connect one NOT gate, one OR gate and one AND gate in Logisim.
04 Verify behavior
Check all eight binary input combinations and record lamp output L.

## Slide 5
Existing systems
05
Approach | Switching basis | Limitation
Manual switching | Operator action | Requires timely action
Fixed timer | Scheduled time | Does not directly sense light
Light-based control | Ambient light level | Needs a defined threshold
Project choice: a digital light-based controller with an enable switch and manual ON override.
Notes: Qualitative design comparison, not an experimental literature survey. The timer and manual alternatives are conceptual baselines. Logic implementation references: https://www.cburch.com/logisim/docs/2.7/en/html/libs/gates/not.html and https://www.cburch.com/logisim/docs/2.7/en/html/libs/gates/basic.html

## Slide 6
Proposed system
06
L = E AND ((NOT D) OR M)
D = 1: daylight E = 1: enabled M = 1: manual ON
E = 0 always switches the lamp OFF.
With E = 1 and M = 0, the lamp follows darkness.
With E = 1 and M = 1, the lamp stays ON.
Notes: The master enable has highest priority. Manual ON is an intentional override and may keep the lamp on during daylight. Source for elementary gate functions: https://www.cburch.com/logisim/docs/2.7/en/html/libs/gates/basic.html

## Slide 7
System architecture
07
Daylight D
NOT
OR
AND
Lamp L
Manual ON M
Enable E
Signal flow runs left to right. The output pin represents the lamp command.
Notes: Editable functional block diagram. D represents a thresholded sensor signal. NOT creates darkness demand, OR includes manual demand, and AND applies master enable.

## Slide 8
Methodology and implementation
08
Input definitions
Use three 1-bit input pins: D, E and M.
Logic stages
Invert D. OR the result with M. AND that result with E.
Lamp indication
Connect the final output to pin L and an LED indicator.
Simulation steps
Open the .circ file, use the Poke tool to toggle inputs, and compare each state with the truth table.
Notes: Circuit target: classic Logisim 2.7.1. All gate inputs use one bit. Official NOT gate reference: https://www.cburch.com/logisim/docs/2.7/en/html/libs/gates/not.html. Official gate reference: https://www.cburch.com/logisim/docs/2.7/en/html/libs/gates/basic.html. Actual simulator execution has not been verified in this environment.

## Slide 9
Results and discussion
09
E | D | M | Expected L
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
Expected logical results
Master disabled: OFF in all four cases.
Automatic mode: ON at night, OFF during daylight.
Manual ON: ON when enabled.
Truth table derived from the equation. Logisim run and output screenshots remain to be recorded.
Notes: These are expected outputs, not measured simulator results. A Python checker in src checks circuit topology and all eight Boolean combinations independently. Record actual Logisim observations in results/simulation_observations.csv.

## Slide 10
Conclusion
10
A three-gate design expresses the complete control rule.
The design supports automatic switching, master disable and manual ON.
The truth table defines the output for every input combination.
Next validation: run the circuit in Logisim and save observed results.
Future hardware: a light sensor with hysteresis and a suitable lamp driver.
Notes: Design and files are prepared. Do not claim physical deployment, measured energy savings or completed Logisim testing without evidence. Hysteresis is a proposed future hardware feature, absent from this digital model.